## Slide 1
SCK (clock) to D2
SIN (serial in, RX) to D3
SOUT (serial out, TX) to D4
GND (ground) to GND
CS to D10paint
MOSI to D11
MISO to D12
SCK to D13
GND to GND
+5 to 5V
Game Boy serial pinout (cable view)
SIN and SOUT are crossed within the serial cable. When you cut it, you do not know which wire is which pin. Use multimeter in continuity mode to identify wires, do not trust the wire colors.

## Slide 2
SCK (clock) to D2
SIN (serial in, RX) to D3
SOUT (serial out, TX) to D4
GND (ground) to GND
Game Boy serial pinout (cable view)
SIN and SOUT are crossed within the serial cable. When you cut it, you do not know which wire is which pin. Use multimeter in continuity mode to identify wires, do not trust the wire colors.
LED to D13

## Slide 3
Printing
Image converted

## Slide 4
Image converted
Printing

## Slide 5
Printing
Image converted

## Slide 6
Arduino proto shield on Arduino SD shield, on Arduino Uno
Open Game Boy serial cable
Game Boy Printer

## Slide 7
Game Boy Printing protocol used
Send INIT command : 88 33 01 00 00 00 01 00 00 00;
Send DATA packet prefix : 88 33 04 00 80 02…
Send 640 bytes of data : …FF FF FF FF FF FF FF FF FF FF FF FF FF FF…
Send DATA packet suffix : …7D 0E 00 00;
Send empty DATA packet : 88 33 04 00 00 00 04 00 00 00;
Send PRINT command : 88 33 02 00 04 00 01 00 E4 7F 6B 01 00 00;
Send INQUIRY command : 88 33 0F 00 00 00 0F 00 00 00;
Magic byte
Checksum LSB first
Bytes into the checksum
Response bytes
Length of data
Bytes red on the SD card (through a memory buffer)
Checksum calculated onboard
Command byte
No compression
1 print
0 margins
Standard palette
Printing intensity (max)
Repeat until OEF on SD card
Repeat 9 times
Length of data, 640 bytes, LSB first
Repeat 9 times, every 1200 ms
keepalive
errors

## Slide 8
Game Boy Printing protocol used
Send INIT command : 88 33 01 00 00 00 01 00 00 00;
Send DATA packet : 88 33 04 00 80 02…DATA…7D 0E 00 00;
Send empty DATA packet : 88 33 04 00 00 00 04 00 00 00;
Send PRINT command : 88 33 02 00 04 00 01 00 E4 7F 6B 01 00 00;
Send INQUIRY command : 88 33 0F 00 00 00 0F 00 00 00;
Magic byte
Checksum
Bytes into
the checksum
Response bytes
Repeat 10 times, every 100 ms
Repeat until end of image
Send INIT command : 88 33 01 00 00 00 01 00 00 00;
Send empty DATA packet : 88 33 04 00 00 00 04 00 00 00;
Send PRINT command : 88 33 02 00 04 00 01 03 E4 7F 6E 01 00 00;
Send INQUIRY command : 88 33 0F 00 00 00 0F 00 00 00;
1 print, margin=0x00, default palette, max printing intensity
Repeat until no image left
Repeat marginx10 times, every 100 ms
1 print, margin=0x03, default palette, max printing intensity
Length of DATA 0x0280
Length of DATA 0x0000
Length of DATA 0x0004
No compression

## Slide 9
Your images
Octave encoder
Game Boy data tile format
SD Card
Arduino
Game boy printer
160x(16*X) pixels
4 shades of gray

## Slide 10
Your images
Octave encoder
Arduino
Game boy printer